## Slide 1
Logic Design
Chapter 5
Synchronous Sequential Logic
(Storage Elements)

## Slide 2
Reading Assignment:
  Digital Design" 6th edition, by Morris Mano and D. Ciletti
  5.2 Sequential Circuits
  5.3 Storage Elements: Latches
  5.4 Storage Elements: Flip‐Flops

## Slide 3: Review: Combinational Circuits
  contains no memory elements
  the outputs depends on the inputs only
3
Combinational Circuit
I
Y = F(I)

## Slide 4: Sequential Circuits
next state
present state
  consists of a combinational circuit to which memory elements are connected to form a feedback path.
  the binary information stored in memory elements defines the state of the sequential circuit at that time.
  (inputs, present state) Þ (outputs, next state)
  two main types of sequential circuits
    synchronous: the transition happens at discrete instants of time
    asynchronous: at any instant of time
4

## Slide 5: Synchronous Sequential Circuits
  a master-clock generator to generate a periodic train of clock pulses
  the clock pulses are distributed throughout the system
  most commonly used
  the memory elements: flip-flops
    binary cells capable of storing one bit of information
    two outputs: one for the normal value and one for the complement value
5

## Slide 6: Storage Element: Latch

## Slide 7: SR Latch :with NORs
7
NOR gate:
‘0’ if either of its inputs are ‘1’
S = set
R = reset
Q = output
S R Q Q’
1 0
0 1
0 0
1 1
1
0
0
1
hold
hold
0
0
Function table
forbidden

## Slide 8: SR Latch :with NORs
8
0
1
1
0
0
0
1
1
0
0
0
1
1
0

## Slide 9: SR Latch :with NORs
Re-examine the inputs S=1 and R=1:
What does it mean to both set and reset at the same time? S-R latch says “both lose!”  Q and Qb both are 0
What happens when S=R=1 (Q=Qb=0) and S or R changes to 0?
  S changes to zero first  Reset wins (Q=0, Qb=1)
  R changes to zero first  Set wins (Q=1, Qb=0)
  Both change at the same time to S=R=0…
R
S
Q
Qb
1
1
When S=R=1 changes to S=R=0, we get an uncontrolled oscillation (unstable)
Moral of the story: S=R=1 is bad  Make it an illegal input
0
0
S
R
Q
Qb
9

## Slide 10: SR Latch :with NANDs
S = set
R = reset
Q = output
S R Q Qb
0 1
1 0
0 0
1 1
1
0
0
1
hold
hold
1
1
10
NAND gate:
‘1’ if either of its inputs are ‘0’
Function table
forbidden

## Slide 11: SR Latch :with NANDs
11
0
1
1
0
0
0
1
1
1
1
0
1
1
0

## Slide 12: SR Latch :with NANDs
Sometimes it is called S’R’ Latch.
The primes designate the fact that the inputs must be in their complement form to activate the circuit.
S’ R’ Q Qb
0 1
1 0
0 0
1 1
1
0
0
1
hold
hold
1
1
12

## Slide 13
SR Latch and S’R’ Latch
An S′R′ latch –with active low set and reset inputs – can be built using NAND gates
An S-R latch –with active high set and reset inputs – can be built using NOR gates
13

## Slide 14: S-R Latch with control input
14

## Slide 15: S-R Latch with control input
C = 1 enables data change
15
C = 0 disables all latch state changes
0
1
1
1
S’
R’
S’R’ Latch

## Slide 16: S-R Latch with control input
16

## Slide 17: D Latch
Input value D is passed to output Q when C is high
Input value D is ignored when C is low
17

## Slide 18
Q
S
R
Clk
D
(Data)
(a) Circuit
Q
t
1
t
2
t
3
t
4
Time
Clk
D
Q
(d) Timing diagram
D-Latch
18

## Slide 19: Symbols for Latches
SR latch is based on NOR gates
S’R’ latch based on NAND gates.
D latch sometimes called transparent latch
19

## Slide 20: Storage Element: Flip-Flop

## Slide 21: Latch v.s. Flip-Flop
The state of a latch or flip-flop is switched by a change of the control input
  Level triggered – latches
  Edge triggered – flip-flops
21

## Slide 22: Edge-Triggered Flip-Flops
Edge-Triggered D Flip-Flop
Edge-Triggered J-K Flip-Flop
Edge-Triggered T Flip-Flop
22

## Slide 23: Edge-Triggered D Flip-Flop
D flops can be triggered on positive or negative edge
Bubble before Clock (C) input indicates negative edge trigger
Lo-Hi edge
Hi-Lo edge
23

## Slide 24
D
Q
Q
D
Q
Q
D
Q
Q
D
Clock
Q
a
Q
b
Q
c
Q
c
Q
b
Q
a
(a) Circuit
Clk
D
Clock
Q
a
Q
b
(b) Timing diagram
Q
c
An Example
24

## Slide 25
Master-Slave D Flip-Flops
Negative edge-triggered D Flip-Flop
Positive edge-triggered D Flip-Flop
25

## Slide 26
D
Q
Q
Master
Slave
D
Clock
Q
Q
D
Q
Q
Q
m
Q
s
D
Clock
Q
m
Q
Q
s
=
(a) Circuit
(b) Timing diagram
Clk
Clk
D
Q
Q
(c) Graphical symbol
Master-Slave D Flip Flop
26

## Slide 27
D
Q
Q
Clock
Appendix: Positive Edge-Triggered D Flip Flop
27
'
'

## Slide 28
The operation of the circuit is as follows.
When Clock = 0
The S and R inputs of the output latch are maintained at the
logic-1. This causes the output to remain in its present state.
When Clock changes to 1
If D = 0, R’ changes to 0. This causes the flip-flop to go to the
reset state, making Q = 0.
After Clock changes to 1, any further changes in D will not affect the output latch as long as Clock = 1
If there is a change in the D input from 0 to 1, R’ remains at 0,
making Q stay at 0.
If there is a change in the D input from 1 to 0, S’ remains at 0,
making Q stay at 1.
28
Appendix: Positive Edge-Triggered D Flip Flop
If D = 1, S’ changes to 0. This causes the flip-flop to go to the
set state, making Q = 1.

## Slide 29
Timing
29
The setup time
  The minimum time that D input must be maintained at a constant value prior to the occurrence of the clock transition.
The hold time
  The minimum time that D input must not change after the occurrence of the clock transition
tsetup
thold
Setup and hold times for negative edge-triggered D Flip-flop

## Slide 30: Asynchronous Inputs
30
Asynchronous inputs that are used to force the flip flop to a particular state independently of the clock.
  Preset (direct set):
    The input that sets the flip-flop to 1.
  Clear (direct reset)
    The input that sets the flip-flop to 0.
When power is turned on, the state of flip-flop is unknown. The direct inputs are used to bring all flip-flops to a known starting state.

## Slide 31: Asynchronous Reset
Note reset signal (R) for D flip flop
If R = 0, the output Q is cleared
This event can occur at any time, regardless of the value of the CLK
31

## Slide 32: Appendix: Asynchronous Reset
32
0
1
1
0

## Slide 33: Parallel Data Transfer
Flip flops store outputs from combinational logic
Multiple flops can store a collection of data
33

## Slide 34
D
Q
Q
Q
Q
J
Clock
(a) Circuit
J
Q
Q
K
0
1
Q
t
1
+
(
)
Q
t
(
)
0
(b) characteristic table
(c) Graphical symbol
K
J
0
0
0
1
1
1
Q
t
(
)
1
K
Positive Edge-Triggered J-K Flip-Flop
34

## Slide 35
Positive Edge-Triggered J-K Flip-Flop
35

## Slide 36
Clock
T
Q
Timing diagram
T
0
1
Q
t
1
+
(
)
Q
t
(
)
Q
t
(
)
Characteristic table
Positive Edge-Triggered T Flip-Flop
36

## Slide 37
Q(t) vs Q(t+1)
37
Positive Edge Triggered
Negative Edge Triggered
Q(t)
Q(t+1)
Q(t)
Q(t+1)
Clk
Output
Clk
Output

## Slide 38
Characteristic Tables
38
    Q(t+1) = D
    Q(t+1) = TQ'+T'Q
    Q(t+1) = JQ'+K'Q

## Slide 39
Characteristic Equations
For D Flip flops
Q(t+1) = D
For JK Flip flops
Q(t+1) = JQ’ + K’Q
For T Flip flops
Q(t+1) = TQ'+T'Q = T  Q
39

## Slide 40: Summary
Flip flops are powerful storage elements
  They can be constructed from gates and latches!
D flip flop is simplest and most widely used
Asynchronous inputs allow for clearing and presetting the flip flop output
Multiple flops allow for data storage
  The basis of computer memory!
Combine storage and logic to make a computation circuit
40
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.