## Slide 1
Logic Design
Chapter 6
Registers and Counters

## Slide 2: Overview
Clocked sequential circuits
  a group of flip-flops and combinational gates
  connected to form a feedback path
  Flip-flops + Combinational gates
  (essential) (optional)
Register:
  a group of flip-flops
  gates that determine how the information is transferred into the register
Counter:
  a register that goes through a predetermined sequence of states
2
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 3: Registers

## Slide 4: Register
A n-bit register
  n flip-flops capable of storing n bits of binary information
  i.e., 4-bit register
Load in parallel on clock transition
  A clock edge applied to the C inputs of flip‐flops will load all four inputs in parallel
Asynchronous Clear
  Clear_b goes to the active‐low R (reset) input of all four flip‐flops
4

## Slide 5: Register Symbol
5
Parallel
Register
A[0]
Clock
A[1]
A[2]
A[3]
I[0]
I[1]
I[2]
I[3]
Clear_b
I[3:0]
A[3:0]
Load
Parallel
Register
Clock
Clear_b
What if signals I[0]~I[3] arrive at different time, due to some combinational circuit delay?

## Slide 6: Register with Load Control
Load’
Load
6
Load = 1
  new data loaded on next positive clock edge
Load = 0
  old data reloaded on next positive clock edge
A0
I0

## Slide 7: Shift Register
a register capable of shifting its binary information in one or both directions
Cascade chain of Flip-Flops
Serial in – Serial out, can also have parallel load / read
7
1 0 1 1 0
initial
1 1 0 1 1
CLK
1 1 1 0 1
CLK
1 1 1 1 0
CLK

## Slide 8: Practice Exercise
8
Practice Exercise 6.1
Draw the logic diagram of a circuit that suspends the clock action of a D flip-flop without gating its clock. Describe the behavior of the circuit.
Answer:
If Data_gate = 1, Data is transferred to Q with each active edge of clock. If Data_gate = 0, the value of Q is recirculated through the mux-flip-flop path, with the effect that clock appears to be suspended.

## Slide 9: Parallel versus Serial
Serial communications is defined as
  Provides a binary number as a sequence of binary digits, one after another, through one data line.
Parallel communications
  Provides a binary number through multiple data lines at the same time.
9

## Slide 10: Serial Transfer from reg A to reg B
Data transfer one bit at a time
Data loopback for register A
Time
Initial value
After T1
After T2
After T3
After T4
Reg A
1011
1101
1110
0111
1011
Reg B
0011
1001
1100
0110
1011
10

## Slide 11: Shift register application
parallel inputs
parallel outputs
serial transmission
Parallel-to-Serial conversion for serial transmission
Serial-to-Parallel conversion for data extraction
11
Shift register
Shift register
Shift register
Shift register

## Slide 12: Universal Shift Register
Capability of a universal shift register:
  A clear control to clear the register to 0.
  A clock input to synchronize the operations.
  A shift-right control to enable the shift right operation and the serial input and output lines associated w/ the shift right.
  A shift-left control to enable the shift left operation and the serial input and output lines associated w/ the shift left.
  A parallel-load control to enable a parallel transfer and the n parallel input lines associated w/ the parallel transfer.
  n parallel output lines.
  A control state that leaves the information in the register unchanged in the presence of the clock.
12

## Slide 13: 4-bit Universal Shift Register
s1 s0 register operation 0 0 No change 0 1 shift right 1 0 shift left 1 1 Parallel load
13

## Slide 14: 4-bit Universal Shift Register
s1 s0 register operation 0 0 No change 0 1 shift right 1 0 shift left 1 1 Parallel load
14

## Slide 15: Serial Addition (D Flip-Flop)
Slower than parallel
Low cost
Only one full adder
Start with low-order bit addition
Shift control start/stop addition
carry (Q) is saved
Add multiple values.
  New values placed in shift register B
15
( i.e. X + Y + Z )

## Slide 16: Serial Addition (D Flip-Flop)
0101
0011
0
0
1
16
We can analyze this serial adder as follows.

## Slide 17: Serial Addition (D Flip-Flop)
0010
?001
17
1
0
1

## Slide 18: Serial Addition (D Flip-Flop)
18
Q(t+1)= D
Q(t)
Or, we can think of this circuit as a finite state machine, implemented with D Flip-flop.
D
    S = x  y  Q
    D = x y + xQ + yQ
(a full adder)

## Slide 19: Serial Addition (JK Flip-Flop)
    JQ = x y
    KQ = x y = (x + y)
    S = x  y  Q
19
The serial adder can be implemented using JK FFs, too.

## Slide 20: Serial Addition (JK Flip-Flop)
    JQ = x y
    KQ = x y = (x + y)
    S = x  y  Q
20

## Slide 21: Summary
Shift registers can be combined together to allow for data transfer
Serial transfer used in modems and computer peripherals (e.g. mouse)
D flip flops allow for a simple design
  Data clocked in during clock transition (rising or falling edge)
Serial addition takes less chip area but is slow
Universal shift register allows for many operations
  The register is programmable.
  It allows for different operations at different times
21
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 22: Counters

## Slide 23: Counters
Counters are important components in computers
  They increment or decrement by one in response to input
Two main types of counters
  Ripple (asynchronous) counters
  Synchronous counters
Ripple counters
  Flip flop output serves as a source for triggering other flip flops
  no common clock pulse (not synchronous)
Synchronous counters
  All flip flops triggered by a common clock signal
Synchronous counters are more widely used in industry.
23
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 24: Ripple Counters

## Slide 25: 4-bit binary ripple Counter
  Binary count sequence: 4-bit
    An n‐bit binary counter consists of n flip‐flops and can count in binary from 0 through 2n - 1.
  To understand the operation of the 4‐bit binary ripple counter, refer to the first nine binary numbers listed in Table 6.4 .
    After the count of 15, the counter goes back to 0 to repeat the count.
A0 is complemented with each count pulse input.
Every time that A0 goes from 1 to 0, it complements A1.
Every time that A1 goes from 1 to 0, it complements A2.
Every time that A2 goes from 1 to 0, it complements A3
25

## Slide 26: 4-bit binary ripple Counters (with JK FFs)
Timing
26

## Slide 27: Problem with ripple Counters
27

## Slide 28: 4-bit binary ripple Counters (with T and D FFs)
1

0
1

0
0
0

1
(From chap5a)
=
28


## Slide 29: Ripple Down-Counter (with JK FFs)
29

## Slide 30: Ripple Down-Counter (with JK FFs)
30

## Slide 31: Ripple UP/Down Counter (with JK FFs)
31

## Slide 32: Ripple Counter (with positive edge-triggered JK FFs)
32

## Slide 33: Modulo ripple Counter
33

## Slide 34: Modulo ripple Counter
34

## Slide 35: BCD Ripple Counter
Q8
Q4
0
0
0
0
0
0
0
0
0
1
0
1
0
1
0
1
Q2
0
0
1
1
0
0
1
1
Q1
0
1
0
1
0
1
0
1
1
0
1
0
0
0
0
1
0
0
0
0
35

## Slide 36: BCD Ripple Counter (method 1)
36

## Slide 37: BCD Ripple Counter (method 2 from Text)
37
Q1: changes state after each clock pulse
Q4: complements every time Q2 goes from 1 to 0.
Q2:
  When Q8=0, Q2 is complemented with Q1 goes from 1 to 0.
  When Q8=1, Q2 =0
Q8:
  When Q2Q4=1, Q8 is complemented with Q1 pulse.
  Q8 is clear when Q2Q4 is 0 with Q1 pulse.
Q8 | Q4 | Q2 | Q1
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
0 | 0 | 0 | 0

## Slide 38: Three-Decade Decimal BCD Counter
To count from 0 to 999, we need a three‐decade counter. Multiple decade counters can be constructed by connecting BCD counters in cascade, one for each decade
When Q8 in one decade goes from 1 to 0, it triggers the count for the next higher order decade.
38

## Slide 39: Synchronous Counters

## Slide 40: Synchronous Counters
Synchronous counter
  A common clock triggers all flip-flops simultaneously
Design procedure
  apply the same procedure of synchronous sequential circuits
  Synchronous counter is simpler than general synchronous sequential circuits
40

## Slide 41: 4-bit synchronous Binary Up-Counter
0
0
1
1
0
1
0
1
0
1
2
3
0
0
1
0
1
0
4
5
6
1
1
7
0
0
0
0
1
1
1
1
Clock cycle
0
0
8
0
Q
2
Q
1
Q
0
Q
1
changes
Q
2
changes
41

## Slide 42: 4-bit synchronous Binary Up-Counter (with T FFs)
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
T
Q
Q
Q
3
42
Rules:
  Qn is complemented when Qn-1……Q1Q0 =1.
  Otherwise, Qn has no change.
Synchronous:
  All flip flops are controlled by the same clock signal.

## Slide 43: 4-bit synchronous Binary Up-Counter (with T FFs)
Clock
Q
0
Q
1
Q
2
Count
0
1
2
3
5
9
12
14
0
(b) Timing diagram
Q
3
4
6
8
7
10
11
13
15
1
T
Q
Q
Clock
T
Q
Q
T
Q
Q
1
Q
0
Q
1
Q
2
(a) Circuit
T
Q
Q
Q
3
43

## Slide 44: 4-bit synchronous Binary Up-Counter (with JK FFs)
Synchronous counters
  All of the FFs are triggered simultaneously by the clock input pulses.
  All FFs change at same time
Remember
  If J=K=0, flop maintains value
  If J=K=1, flop toggles
Most counters are synchronous in computer systems.
Can also be made from D flops
  Value increments on positive edge
44

## Slide 45: 4-bit synchronous Binary Down-Counter (with JK FFs)
45
Q8 Q4 Q2 Q1
1 1 1 1
1 1 1 0
1 1 0 1
1 1 0 0
1 0 1 1
1 0 1 0
1 0 0 1
1 0 0 0
Down

## Slide 46: 4-bit synchronous Binary Up/Down Counter (with T FFs)
Up/Down Counter can either count up or down on each clock cycle
Up counter counts from 0000 to 1111 and then changes back to 0000
Down counter counts from 1111 to 0000 and then back to 1111
Counter counts up or down each clock cycle
Output changes occur on clock rising edge
46

## Slide 47: Counters with Parallel Load
Counters with parallel load can have a preset value
Load signal indicates that data (I3…I0) should be loaded into the counter
Clear resets counter to all zeros
Carry output could be used for higher-order bits
Clear Clk Load Count Function
0 X X X Clear to 0
1 ↑ 1 X Load inputs
1 ↑ 0 1 Count
1 ↑ 0 0 No Change
47

## Slide 48: Practice Exercise
48
Practice Exercise 6.3
How do a ripple counter and a synchronous counter differ in their behavior?
Answer:
All of the flip-flops in a synchronous counter are synchronized by receiving a common clock pulse; only the first stage of a ripple counter receives a clock pulse.
The stages of a synchronous counter are updated simultaneous by a common clock; the stages of a ripple counter are updated one at a time.
A synchronous counter operates faster than a ripple counter.

## Slide 49: Other Synchronous Counters

## Slide 50: Divide-by-4 clock frequency divider
50
fQ1 = 1/4 fclock
fQ0 = 1/2 fclock
fQ1 = 1/2 fQ0

## Slide 51: BCD Counters Implemented by Binary Counter
51
Clear Clk Load Count Function
0 X X X Clear to 0
1 ↑ 1 X Load inputs
1 ↑ 0 1 Count
1 ↑ 0 0 No Change

## Slide 52: BCD Synchronous Counter
To derive the circuit of a BCD synchronous counter, it is necessary to go through a sequential circuit design procedure.
The state table of a BCD counter is listed in Table 6.5 . The input conditions for the T flip‐flops are obtained from the present‐ and next‐state conditions. An output y which is equal to 1 when the present state is 1001.
52

## Slide 53: Counter with Unused States
Consider the counter specified in Table 6-7
Two unused states: 011 & 111
JA = B KA = B
JB = C KB = 1
JC = B’ KC = 1
The simplified equations are
53

## Slide 54: Counter with Unused States
54

## Slide 55: Self Correcting
55
Self-correcting counter
  Ensure that when a clock enter one of its unused states, it eventually goes into one of the valid states after one or more clock pulses so it can resume normal operation.
ABC=111  ABC=000
JA = 1, KA = 1 A=0
JB = 1, KB = 1 B=0
JC = 0, KC = 1 C=0
ABC=011  ABC=100
JA = 1, KA = 1 A=1
JB = 1, KB = 1 B=0
JC = 0, KC = 1 C=0

## Slide 56: Ring Counter
A ring counter is a circular shift register with only one flip-flop being set at any particular time, all others are cleared.
(initial value = 1 0 0 … 0 )
The single bit is shifted from one flip-flop to the next to produce the sequence of timing signals.
56

## Slide 57: Ring Counter
Application of counters
  Counters may be used to generate timing signals to control the sequence of operations in a digital system.
Approaches for generation of 2n timing signals
  1. a shift register with 2n flip-flops
  2. an n-bit binary counter together with an n-to-2n-line decoder
57

## Slide 58: Johnson Counter
A k-bit Johnson counter will go through a sequence of 2k states.
58

## Slide 59: Sequence of Timing Clock
59
0000
1000
1100
1110
1111
0111
0011
0001
1 0 0 0 0 0 0 0
0 1 0 0 0 0 0 0
0 0 1 0 0 0 0 0
0 0 0 1 0 0 0 0
0 0 0 0 1 0 0 0
0 0 0 0 0 1 0 0
0 0 0 0 0 0 1 0
0 0 0 0 0 0 0 1

## Slide 60: Comparision
60
Using binary counter
  Need a 3-bit binary counter together with a 3-to-8 decoder
Using ring counter
  Need an 8-bit ring counter
Using Johnson counter
  Need a 4-bit johnson counter
  and simple decoding circuit
To generate repeated 8 different timing signals:
T0
T1
T2
T3
T4
T5
T6
T7

## Slide 61: Summary
Binary counters can be ripple or synchronous
Ripple counters use flip flop outputs as flip flop triggers
  Some delay before all flip flops settle on a final value
Synchronous counters are controlled by a clock
  All flip flops change at the same time
Up/Down counters can either increment or decrement a stored binary value
  Control signal determines if counter counts up or down
Counters with parallel load can be set to a known value before counting begins.
61
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.